Regulator:

Status:
Removed from 1l_15

Issue faced:
The regulated voltage would go as low as 2.8 thus not providing suffient energy supply.

Solution:
The ESP-01 module shall act as the battery monitor. Once the battery reaches below a certain threshhold, the ESP shall trade irrcorrigible data. This is the cue for the controller to shut down every peripheral and glow the “CHARGE REQUIRED” LED.

Charger IC:

Staus:
Shift from MCP73838 to MCP73831

Issue Faced:
The MCP73838 created a lot of problems, each time it was connected / used in a new circuit. The exact technical reason is not known.

Solution:
MCP73831 was tested for reliability and repetability. It also provides better charging speed.